## Slide 1: The Datalink Layer Chapter 3
How to transmit information among two machines between two adjacent machines in a reliable and efficient manner?
  Conceptually two machines are connected like a wire (coaxial cable, telephone line, or wireless channel)
  There is a non-zero propagation delay
  Communication channel makes errors

## Slide 2: The Data Link Layer
Application Transport
Responsible for delivering frames of information over a single link
Handles transmission errors and regulates the flow of data
Provides well-defined service to network layer
Dealing with transmission errors
Regulates data between high-speed sender and slow speed receiver
Network Link Physical

## Slide 3: Outline
Data Link Layer Design Issues
Error Detection and Correction
Elementary Data Link Protocols
Sliding Window Protocols
Example Data Link Protocols

## Slide 4: Data Link Layer Design Issues
Frames »
Possible services »
Framing methods »
Error control »
Flow control »

## Slide 5: Frames
Link layer accepts packets from the network layer, and encapsulates them into frames that it sends using the physical layer; reception is the opposite process
Network
Link
Virtual data path
Actual data path
Physical

## Slide 6: Possible Services
Unacknowledged connectionless service
Frame is sent with no connection / error recovery
Ethernet is an example
Acknowledged connectionless service
Frame is sent with retransmissions if needed
Example is 802.11 (WiFi)
Acknowledged connection-oriented service
  First phase: Connection is set-up
  Second phase: Frames are transmitted
  Third phase: connection is released.

## Slide 7: Framing Methods
Datalink layer must use services provided by physical layer
  The physical layer may add some redundant signals, but the transmission may not be not error free
  It is up to datalink layer to detect, if necessary, correct errors.
Approach
  Break the bitstream into discrete frames, compute the checksum and include checksum with the frame. When the frame arrives, checksum is recomputed. If it is different, steps will be taken to deal with the issue.
Four methods of framing
  Byte count »
  Flag bytes with byte stuffing »
  Flag bits with bit stuffing »
  Physical layer coding violations
    Use non-data symbol to indicate frame

## Slide 8: Framing – Byte count
Frame begins with a count of the number of bytes in it
Simple, but difficult to resynchronize after an error
Expected
case
Error case

## Slide 9: Framing – Byte stuffing
Special flag bytes delimit frames; occurrences of flags in the data must be stuffed (escaped), at the both end of frame
Longer, but easy to resynchronize after error
Frame format
Need to escape extra ESCAPE bytes too!
Stuffing examples

## Slide 10: Framing – Bit stuffing
Stuffing done at the bit level:
Frame flag has six consecutive 1s (not shown)
On transmit, after five 1s in the data, a 0 is added
On receive, a 0 after five 1s is deleted
Data bits Transmitted bits
with stuffing

## Slide 11: About Error Control
Issue: How to make sure all frames are eventually delivered to the network layer in order?
For connectionless service, it is OK if the sender keeps sending the frames continuously
However, for reliable, connection-oriented service, it would not be fine at all.
Approach
  Error control repairs frames that are received in error
  Requires errors to be detected at the receiver
  Feedback in terms of positive and negative acks.
  Timer protects against lost acknowledgements
  Typically retransmit the unacknowledged frames
  When frames are transmitted multiple times, there is an issue
    Assign sequence numbers

## Slide 12: Design Issue: Flow Control
How to prevent a fast sender from out-pacing a slow receiver?
Feedback based flow control
  Receiver sends back information to the sender giving it the permission to send the data
Rate-based flow control
  Built-in mechanism that limits the rate.
Overall, a set of well-defined rules are formed
Receiver gives feedback on the data it can accept
Flow control is a topic in the Link and Transport layers.

## Slide 13: Error Detection and Correction
Error codes add structured redundancy to data so errors can be either detected, or corrected.
Error correction codes:
Hamming codes »
Binary convolutional codes »
Reed-Solomon and Low-Density Parity Check codes
− Mathematically complex, widely used in real systems
Error detection codes:
Parity »
Checksums »
Cyclic redundancy codes »

## Slide 14: Error Bounds – Hamming distance
Code turns data of n bits into codewords of n+k bits
Hamming distance is the minimum bit flips to turn one valid codeword into any other valid one.
Example with 4 codewords of 10 bits (n=2, k=8):
− 0000000000, 0000011111, 1111100000, and 1111111111
− Hamming distance is 5
Bounds for a code with distance:
2d+1 – can correct d errors (e.g., 2 errors above)
d+1 – can detect d errors (e.g., 4 errors above)

## Slide 15: Error Correction – Hamming code
Hamming code gives a simple way to add check bits and correct up to a single bit error:
•
•
Check bits are parity over subsets of the codeword Recomputing the parity sums (syndrome) gives the
position of the error to flip, or 0 if there is no error
(11, 7) Hamming code adds 4 check bits and can correct 1 error

## Slide 16: Error Correction – Convolutional codes
Operates on a stream of bits, keeping internal state
Output stream is a function of all preceding input bits
Bits are decoded with the Viterbi algorithm
… 1 1 1
… 1 0 0 1 1 1
Popular NASA binary convolutional code (rate = ½) used in 802.11

## Slide 17: Error Detection – Parity (1)
Parity bit is added as the modulo 2 sum of data bits
Equivalent to XOR; this is even parity
Ex: 1110000  11100001
Detection checks if the sum is wrong (an error)
Simple way to detect an odd number of errors
•
•
Ex: 1 error, 11100101; detected, sum is wrong Ex: 3 errors, 11011001; detected sum is wrong
Ex: 2 errors, 11101101; not detected, sum is right!
Error can also be in the parity bit itself
Random errors are detected with probability ½

## Slide 18: Error Detection – Parity (2)
Interleaving of N parity bits detects burst errors up to N
Each parity sum is made over non-adjacent bits
An even burst of up to N errors will not cause it to fail

## Slide 19: Error Detection – Checksums
Checksum treats data as N-bit words and adds N check bits that are the modulo 2N sum of the words
Ex: Internet 16-bit 1s complement checksum
Properties:
Improved error detection over parity bits
Detects bursts up to N errors
Detects random errors with probability 1-2N
Vulnerable to systematic errors, e.g., added zeros

## Slide 20: Error Detection – CRCs (1) Cyclic Redundancy Checks
Adds bits so that transmitted frame viewed as a polynomial is evenly divisible by a generator polynomial
Start by adding 0s to frame and try dividing
Offset by any reminder to make it evenly divisible

## Slide 21: Error Detection – CRCs (2)
Based on standard polynomials:
Ex: Ethernet 32-bit CRC is defined by:
Computed with simple shift/XOR circuits Stronger detection than checksums:
E.g., can detect all double bit errors
Not vulnerable to systematic errors

## Slide 22: Elementary Data Link Protocols
Link layer environment »
Utopian Simplex Protocol »
Stop-and-Wait Protocol for Error-free channel »
Stop-and-Wait Protocol for Noisy channel »

## Slide 23: Link layer environment (1)
Commonly implemented as NICs (Network Interface Cards) and OS drivers; network layer (IP) is often OS software

## Slide 24: Link layer environment (2)
Link layer protocol implementations use library functions
See code (protocol.h) for more details
Group | Library Function | Description
Network layer | from_network_layer(&packet) to_network_layer(&packet) enable_network_layer() disable_network_layer() | Take a packet from network layer to send Deliver a received packet to network layer Let network cause “ready” events Prevent network “ready” events
Physical layer | from_physical_layer(&frame) to_physical_layer(&frame) | Get an incoming frame from physical layer Pass an outgoing frame to physical layer
Events & timers | wait_for_event(&event) start_timer(seq_nr) stop_timer(seq_nr) start_ack_timer() stop_ack_timer() | Wait for a packet / frame / timer event Start a countdown timer running Stop a countdown timer from running Start the ACK countdown timer Stop the ACK countdown timer

## Slide 25: Utopian Simplex Protocol
An optimistic protocol (p1) to get us started
Assumes no errors, and receiver as fast as sender
Considers one-way data transfer
}
Sender loops blasting frames Receiver loops eating frames
That’s it, no error or flow control …

## Slide 26: Stop-and-Wait – Error-free channel
Protocol (p2) ensures sender can’t outpace receiver:
Receiver returns a dummy frame (ack) when ready
Only one frame out at a time – called stop-and-wait
We added flow control!
Sender waits to for ack after
Receiver sends ack after passing
passing frame to physical layer
frame to network layer

## Slide 27: Stop-and-Wait – Noisy channel (1)
’
ARQ (Automatic Repeat reQuest) adds error control
Receiver acks frames that are correctly delivered
Sender sets timer and resends frame if no ack.
For correctness, frames and acks must be numbered
Else receiver can t tell retransmission (due to lost ack or early timer) from new frame
For stop-and-wait, 2 numbers (1 bit) are sufficient

## Slide 28: Stop-and-Wait – Noisy channel (2)
{
Sender loop (p3):
Send frame (or retransmission) Set timer for retransmission Wait for ack or timeout
If a good ack then set up for the next frame to send (else the old frame will be retransmitted)

## Slide 29: Stop-and-Wait – Noisy channel (3)
Receiver loop (p3):
Wait for a frame
If it’s new then take it and advance expected frame
Ack current frame

## Slide 30: Sliding Window Protocols
Sliding Window concept »
One-bit Sliding Window »
Go-Back-N »
Selective Repeat »

## Slide 31: Sliding Window Protocols
In the previous protocols, data frames are transmitted in one direction only
In most practical situations, data frames have to be transmitted in both directions.
Each link has a forward channel and reverse channel. The capacity of reverse channel is wasted.
Alternative
  Use the same link in both directions.
  Data frames of A and B are intermixed with ack frames of A and B.
Piggybacking
  Temporarily delaying ack so that they can be hooked into the next outgoing frame.
However, piggybacking increases the delay.
  Use hybrid
    If possible use piggybacking otherwise send a separate ack frame.

## Slide 32: Sliding Window Protocols
Summary of sliding window protocols
  Sender maintains a sequence numbers for frames (sending window)
  Receiver also maintains a receiving window.
  Whenever a packet is received from network layer, it gives a highest sequence number and the upper edge of the window is advanced by one.
  When ack, arrives lower edge of the window is advanced by one.
  Sender needs n buffers to hold unack frames

## Slide 33: Sliding Window concept (2)
A sliding window advancing at the sender and receiver
Ex: window size is 1, with a 3-bit sequence number.
Sender
Receiver
At the start
First frame is sent
First frame is received
Sender gets first ack

## Slide 34: Sliding Window concept (3)
Larger windows enable pipelining for efficient link use
Stop-and-wait (w=1) is inefficient for long links
Best window (w) depends on bandwidth-delay (BD)
Want w ≥ 2BD+1 to ensure high link utilization
Pipelining leads to different choices for errors/buffering
We will consider Go-Back-N and Selective Repeat

## Slide 35: One-Bit Sliding Window (1)
Transfers data in both directions with stop-and-wait
Piggybacks acks on reverse data frames for efficiency
Handles transmission errors, flow control, early timers
{
Each node is sender and receiver (p4):
Prepare first frame
Launch it, and set timer
. . .

## Slide 36: One-Bit Sliding Window (2)
. . .
Wait for frame or timeout
If a frame with new data then deliver it
If an ack for last send then
prepare for next data frame
(Otherwise it was a timeout)
Send next data frame or retransmit old one; ack the last data we received

## Slide 37: One-Bit Sliding Window (3)
Two scenarios show subtle interactions exist in p4:
− Simultaneous start [right] causes correct but slow operation compared to normal [left] due to duplicate transmissions.
Time
Notation is (seq, ack, frame number). Asterisk indicates frame accepted by network layer .
Normal case Correct, but poor performance

## Slide 38: Go-Back-N Sliding window protocol
Receiver only accepts/acks frames that arrive in order:
Discards frames that follow a missing/errored frame
Sender times out and resends all outstanding frames

## Slide 39: Go-Back-N Protocol
Tradeoff made for Go-Back-N:
Simple strategy for receiver; needs only 1 frame
Wastes link bandwidth for errors with large windows; entire window is retransmitted
Implemented as p5 (see code in book)

## Slide 40: Selective Repeat Sliding Window Protocol
Receiver accepts frames anywhere in receive window
Cumulative ack indicates highest in-order frame
NAK (negative ack) causes sender retransmission of a missing frame before a timeout resends window

## Slide 41: About Selective Repeat
Tradeoff made for Selective Repeat:
More complex than Go-Back-N due to buffering at receiver and multiple timers at sender
More efficient use of link bandwidth as only lost frames are resent (with low error rates)
Implemented as p6 (see code in book)

## Slide 42: Selective Repeat
For correctness, we require:
Sequence numbers (s) at least twice the window (w)
Error case (s=8, w=7) – too few sequence numbers
Correct (s=8, w=4) – enough sequence numbers
Originals
Originals
Retransmits
Retransmits
New receive window overlaps old – retransmits ambiguous
New and old receive window don’t overlap – no ambiguity

## Slide 43: Example Data Link Protocols
Packet over SONET (Synchronous Optical Network (SONET)
PPP (Point-to-Point Protocol) »
ADSL (Asymmetric Digital Subscriber Loop) »

## Slide 44: Packet over SONET
Packet over SONET is the method used to carry IP packets over SONET optical fiber links
Uses PPP (Point-to-Point Protocol) for framing
Protocol stacks
PPP frames may be split over SONET payloads

## Slide 45: PPP (1)
PPP (Point-to-Point Protocol) is a general method for delivering packets across links
Framing uses a flag (0x7E) and byte stuffing
“Unnumbered mode” (connectionless unacknow- ledged service) is used to carry IP packets
Errors are detected with a checksum
IP packet
0x21 for IPv4

## Slide 46: PPP (2)
A link control protocol brings the PPP link up/down
State machine for link control

## Slide 47: ADSL (1)
Widely used for broadband Internet over local loops
ADSL runs from modem (customer) to DSLAM (ISP)
IP packets are sent over PPP and AAL5/ATM (over)

## Slide 48: ADSL (2)
PPP data is sent in AAL5 frames over ATM cells:
ATM is a link layer that uses short, fixed-size cells (53 bytes); each cell has a virtual circuit identifier
AAL5 is a format to send packets over ATM
PPP frame is converted to a AAL5 frame (PPPoA)
AAL5 frame is divided into 48 byte pieces, each of which goes into one ATM cell with 5 header bytes

## Slide 49: Chapter 3
End